## Slide 1: Path Planning for Manipulator Arm Mounted on Mobile Robot Base
RBE502 Term Project
Kyle Cantrell, Craig miller, Jordan nelson

## Slide 2: Objectives
Dynamical Model
Closed-Loop Control in MATLAB
  Manipulator Arm
  Mobile Robot Base
Calculate Joint Torques in MATLAB
Simulate robot performance in ROS
Gather experimental data
Compare analytical, simulated, and experimental data

## Slide 3: INTRODUCTION
Application of Mobile Robots with Manipulators is growing
Understanding these specific systems is greatly beneficial to robotics engineers due to the practical application of robotics in a critical environment.
This tasking has been examined before but this case is a comparison between what ROS is communicating and what our team can generate from similar mathematical models (MATLAB)
Key components are ROS, RVIZ and MATLAB.

## Slide 4: Robot models: turtlebot waffle pi
Differential-Drive Mobile Robot
Supported by ROS Community
Kinematics & Dynamics are well-understood

## Slide 5: Robot models: openmanipulator
4 DOF Manipulator Arm
Supported by ROS Community
Kinematics & Dynamics are well-understood
Can be mounted directly on TurtleBot Waffle Pi

## Slide 6: Robot models: openmanipulator with turtlebot waffle pi
Most simple option capable of achieving our goal
Ideal candidate for our project
  OpenSource Projects
  3D Model Availability
  ROS Unified Robot Description Format (URDF) Models
Research reproducibility

## Slide 7: Simulation: overview
Realistic application
  Waffle-Pi executes “Pick and Place” maneuver
Leverage all areas of knowledge learned in RBE502
  Uses Path and Trajectory Planning/Control
  Mobile and Manipulator type robots
Simulated in Gazebo and MATLAB
  Gazebo allows full system simulation (LIDAR, SLAM, Dynamixel Actuators, wheel slippage)
  MATLAB allows full simulation of individual parts (Mobile and Arm), but without visual and dynamical systems described by cad design files.
Results evaluated in MATLAB then ROS/Gazebo
Notes: Simulation was chosen to encompass all areas touched in RBE502 on a popular robotic configuration (Mobile base with arm)
In particular, areas used, path and trajectory planning, PID Control, trajectory tracking control, arm and error dynamics
Simulations done twice in Gazebo and Matlab to evaluate physical and algorithmic response in Gazebo along with the dynamical systems response in MATLAB
The scenario is a typical “Pick and Place” scenario detailing a maneuver in cartesian space over to an object in a specific pose, once the goal destination is reached, the arm is operated to interact with the object

## Slide 8: CONTROL METHODS: MOBILE ROBOT BASE (Simulation)
Differential Drive Mobile Robot (DDMR)
Used error dynamics with trajectory tracking
“Effort” is split between number of wheels (2 in this case)
Dynamical Model derived from literature, but cartesian control makes the dynamical model unnecessary for trivial cases

## Slide 9: CONTROL METHODS: MOBILE ROBOT BASE (Experimental/ROS)
Still Differential Drive Mobile Robot (DDMR)
Uses Dynamic Windowed Approach with input from LIDAR mounted on top of robot
  Series of intermediate trajectories “simulated” in ROS, scored, then executed
  Part of Global Plan
Cost Maps are generated, updated and maintained in order to provide an optimized path between current position and “goal”
Notes: Same DDMR model
Uses Gazebo (Robotics Physics Simulation Software) to produce realistic data
LIDAR data is simulated in a standard package “room” world, producing point cloud data off the virtual walls
LIDAR data is processed and fed into the DWA (Dynamic Windowed Approach Algorithm)
The DWA Algorithm simulates possible trajectories toward an end goal and ranks them in order to determine the best intermediate course of action
Once the best course of action is chosen, it is executed and associated SLAM Cost maps are updated and recalculated to reflect the current state of the robot and how it relates to the “goal position”

## Slide 10: Control methods: manipulator arm
Initially attempted PD Control +Feedforward
Ended up deciding on using PID Controller.
Positives:
Most industrial robots utilize PID control
Good overall performance
Negatives:
Tuning is non-trivial

## Slide 11: CONTROL METHODS: MANIPULATOR ARM (ROS/Experimental)
Uses “open_manipulator_position_control”
  Leverages PID Control with experimentally determined gains from ROBOTIS
Ideally is already “tuned”
Controller is abstracted from the user so position/pose are the only parameters necessary
IKFast used for inverse kinematics solving (~5 microsecond deterministic timing on modern processors)
Notes: Readily available ROS package “open_manipulator_position_control”
Position control was chosen as the low-end requirement to pick an object up and place it somewhere else
The arm comes ”pre-tuned” from ROBOTIS, experimentally determined gains
Software in ROS/Robotis is so advanced that position and pose are the only input parameters from our system
Includes a “gripper” to pick things up and subsequent independent control
Handles all inverse kinematics through ROS plugin, Ikfast which has microsecond ranges for up to 7 DoF arms

## Slide 12: simulation: matlab OpenManipulator
Manipulator Arm – PID Control
The manipulator arm was moved from state 1 to 2 and back
The following data was recorded and logged:
Joint Velocities vs Time
Joint Positions vs Time
End Effector Position vs Time
Position Error vs Time
And compared with ROS data.

## Slide 13
Ros simulation: om with tb3

## Slide 14
ROS node plot

## Slide 15
Ros coordinate frame tree
Notes: This is an example of a ROS COORDINATE FRAME TREE detailing the hierarchical structure of all transforms and mechanical connections in the turtlebot from each individual castor to the links of the manipulator arm

## Slide 16: experiment
TurtleBot Burger
  Too small to support OpenManipulator
  ROS Controlled
  Python listener file
Setup
  Map of environmental generated with SLAM
  Three markers placed at key positions

## Slide 17
Experimental: Turtlebot burger

## Slide 18: Results: mobile robot

## Slide 19: Results: manipulator arm

## Slide 20: conclusion
Discussion
  Successful path planning for manipulator arm in MATLAB
  Successful simulations in ROS for integrated robot
  Retrieved odometry data from ROS Simulations & live experiment
Lessons Learned
  Error Dynamics model for Mobile Robot
Future Work
  More accurate analytical models for mobile robot
  ROS Gains
  Experimental data from OpenManipulator with TurtleBot Waffle Pi